## Slide 1
Anchor traffic resolution to a control decision
Model-first risks unnecessary detail and a task chosen to fit it.
Choose model
Implement
Find task
Working line: establish decision value before choosing richer traffic state.
Task + baseline
Hidden-state value?
State + gradients
Notes: Purpose: move from a model-first development sequence to task-anchored methodological design. Starting question: what traffic resolution is necessary for credible, useful control gradients? The current urban simulator is not a fixed constraint on the independent freeway branch. The top sequence presents the risks of choosing detail before evidence; it does not claim earlier implementation was invalid. The bottom sequence states the conditional working line: task and strong baseline, hidden-state decision value, then justified state refinement and separate gradient tests.
Sources: ../differentiable_freeway_bottleneck_task_pre_review/pre_review_closure_and_handoff.md, sections3 P1-P7; ../differentiable_freeway_bottleneck_task_review/01_review_recap_through_s06.md, section1.
Working-line amendment: the lower sequence replaces the earlier construction diagram. The control task defines the comparison; the strongest aggregate alternative determines what must be hidden; a useful decision difference, not richer forward behavior alone, conditionally justifies added state. Refinement and gradient tests are later obligations, not approved construction. Next slide fixes the task, objective and baseline.

## Slide 2
A narrowing makes the question concrete
One speed recommendation for all lanes
Continuing lanes
Ending lane
Advice changes desired speed; traffic interactions determine actual motion.
Strong baseline: spatial traffic, mean response, queues and full history.
Outcome: total travel and waiting time, including upstream queues.
Next: what can the strongest aggregate baseline already explain?
Notes: The operational anchor is an exogenous freeway lane reduction. Initial prospective reference: homogeneous permanent three-to-two narrowing. One infrastructure speed recommendation is shared by all lanes in the advice zone and changes desired free speed; actual motion remains endogenous. No direct vehicle trajectories, forced lane changing or differentiated lane actions. Source mass and waiting must not disappear at the observation boundary. Temporary closure conclusions additionally need reopening and recovery accounting.
Sources: review recap section1; reporting/s01_30_n1_user_gate.md; reporting/s02_35_feedback23_task_and_minimum_information_response.md, section2. Diagram is conceptual, not a simulated road trajectory.
Logical hand-off: common actions and full waiting accounting make the control comparison meaningful. Before attributing value to lane information, review the strongest aggregate response/history alternative; a weak baseline would confound the root question.

## Slide 3
What literature does—and does not—justify
Aggregate response + history
Strong baseline—not full obedience
Lane distribution + transfer
Mechanism evidence—not necessity
Richer-model control gains
Check action/objective confounds
Classes, lanes and individual order are not a mandatory development ladder.
Next: match full aggregate history, advice choices and objective.
Notes: Combines task framing and predecessor/contrast reviews. Strong aggregate response/history is already credible: Frejo2019 calibrates mean response, Wei2025 retains entry-speed history. Lane transfer models establish plausible behavior, not minimum-information necessity. Seliman2020 macro/micro reoptimization changes objectives, search effort and sometimes actions; Chen2025 lane CTM/MPC compares VSL/no-VSL, not state-only usefulness under the same shared advice. Fixed classes and individual order remain conditional. No first-of-kind or global absence claim.
Sources: reporting/s02_20_n2_findings_and_gate.md sections3-5; reporting/s02_36_feedback23_amendment_novelty_and_component_necessity.md; reporting/s03_20_rb_findings_and_gate.md. Primary anchors: https://doi.org/10.1016/j.trc.2019.01.001 ; https://doi.org/10.1111/mice.13492 ; https://doi.org/10.1061/JTEPBS.0000395 ; https://doi.org/10.1016/j.physa.2025.130876 .
Logical hand-off: because aggregate response/history already explains important behavior, and richer-control comparisons can change actions or objectives, the next step isolates information value. Equal totals alone are inadequate: the declared retained history must match, with the same advice menu and cost definition. Classes, lanes and order remain conditional rather than assumed necessities.

## Slide 4
Lane differences need not change decisions
Illustration only: equal totals, not a certified full-history match.
Situation 1
15
15
Situation 2
5
25
Ending lane
Continuing lanes
Required: match the complete retained aggregate observations and history.
Information loss: identical inputs still conceal decision-relevant differences.
Model inadequacy: available information is used poorly by one model.
Decision-loss test: no common acceptable advice in the tested menu.
Next: can hidden lane state alter the value of common advice?
Notes: Illustrative contrast, not a reachable matched-history result. Both totals are30 vehicle-equivalents; ending/continuing group totals are15/15 versus5/25. Continuing lanes are combined for illustration, so this is not a sufficient-state claim. Matching totals alone is weak: the exact-information claim requires equality of the declared strong spatial observation/history channel. Hidden past lane-entry allocations are different unknown past forcing. A particular observer's failure is a distinct model-quality claim. Distinct best actions or a pairwise ranking reversal is insufficient if another common acceptable action exists. Finite-menu evidence does not establish continuous-space or feedback-policy necessity.
Sources: reporting/s04_20_rb_diagnostic_methodology_findings_and_gate.md and recap sections1/S04; current review's lane-contrast explanation. No plot data were measured or simulated.
Logical hand-off: the matched-history contract states what would count as lost information, but does not establish that such information changes useful advice. The next analytical step must jointly supply hidden contrast and decision relevance, including the possibility of a common acceptable action.

## Slide 5
Hidden state must change useful decisions
Shared advice
Desired speed
Merging
Outcome?
Hidden contrast is possible in conditional free flow—but that is not enough.
Fixed-service subcase: earlier arrivals make highest advice a common best.
Thus inspect native merging: can state-dependent benefits outweigh delay?
Next: find a reachable hidden-state contrast with different useful advice.
Notes: Conditional original deductions: conservative transfers cancel from aggregate mass in a homogeneous free-flow branch, allowing an early hidden lane contrast without certifying native near-drop preparations. In the separate work-conserving fixed-service subcase, advice-independent service and fastest-arrival dominance make highest advice a common best action, with source/approach waiting counted. This is not universal no-benefit from speed advice. Need endogenous service/receiving/propagation or failure of arrival dominance plus hidden-state dependence and benefit exceeding slowing delay. Native coupling is mechanism evidence only, not a proof that advice is beneficial. A missing held-highest-advice stress probe can leave a common better action outside a pulse menu.
Sources: reporting/s05_20_rb_certificate_findings_and_gate.md; synthesis/rb_certificate_analysis.pdf; reporting/s06_20_reference_bridge_findings_and_gate.md. Native model: Jakob Erdmann2015, https://elib.dlr.de/102254/1/Springer-SUMOs_Lane_changing_model.pdf . No borrowed discrete resets, random mass shifts, smoothing or invented penalty is approved.
Logical hand-off: the hidden-state construction and fixed-service obstruction are separate conditional deductions, not a combined native certificate. They explain why the subsequent reference-first review inspects endogenous merge interactions rather than inserting an arbitrary penalty. A credible mechanism must still be instantiated in reachable preparations with matched declared history and no common acceptable advice.

## Slide 6
Mechanisms exist; information value is open
Supported: strong aggregate alternatives and plausible merge mechanisms.
Missing: a reachable full-history match requiring different useful advice.
Earlier upstream
Near the narrowing
Next: make the contrast reachable without omitting informative history.
If useful advice must differ, test the smallest conservative added state.
Then test gradient correctness and independent usefulness separately.
Without that evidence, do not infer that richer traffic detail is necessary.
Notes: Current synthesis: no complete positive or negative conclusion for the joint information-to-useful-advice claim. Advisory aggregate-feedback benefits (FB0005) and occupancy-conditioned lane fractions (FB0039) strengthen the aggregate alternative, without proving sufficiency. Native gap/speed/cooperation and field redistribution are precedents, not minimum-state or useful-gradient evidence. Strong regulatory low-speed lane-drop outcomes (Zhang2023) do not transfer automatically to moderate voluntary advice. Preparation must be reachable and survive native anticipation; later interaction may expose the difference in mean-speed/history. The proposed40/60s times cannot reach the final400m under intended road-start/speed bounds;80s remains sparse under conditional entry defaults. No server/simulation result was used. Diagram shows the semantic tension between earlier hidden information and near-merge consequences, not an approved scenario change.
Sources: reporting/s06_20_reference_bridge_findings_and_gate.md; extraction/s06_reference_mechanism_source_audit.md; recap section3. New primary lane-drop manuscript: https://ira.lib.polyu.edu.hk/bitstream/10397/92568/1/Zhang_Optimization_Speed_Freeway.pdf . Future minimal-refinement, forward, internal gradient and independent usefulness obligations remain separate. Review/communication does not authorize construction or experiments.
Logical synthesis: source-supported mechanisms do not close the joint witness. The remaining review step concerns reachable contrast preparation under the full retained-history contract. Only a demonstrated decision-value witness can motivate the smallest conservative refinement; forward fidelity, gradient correctness and independent control usefulness then require distinct evidence. Failure to find a witness is not a global sufficiency theorem. Current review gate remains open; this deck amendment approves neither a preparation change nor any experiment.