## Slide 1
Ramp metering: what should models retain?
From information hiding to an adequate prediction model
Weekly methodology review · 9 October 2026
One local ramp merge · common rate decisions · complete system time
Source review and analytical checks; the research task remains open.
Notes: Request 7, week ending 9 October 2026. Continue from last week's mass/flow information-hiding obstruction through the completed D2 forward-contract continuation. Slides 3--10 are the group-meeting backbone; 11--14 are technical discussion pages. This deck synthesizes existing source/static review, not a simulation or a new scientific pass. The review is temporarily parked at Q.J.F.R; preserving the full field is recommended but unapproved.
Sources:
temp_content/feedback/feedback.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/d2_forward/findings_and_field_gate.md

## Slide 2
Contents
Group meeting · slides 3–10
Why the original information claim stalled
What backtracking changed, and what the new chain establishes
Technical discussion · slides 11–14
Creation and recovery; shared service; spatial fields; control evidence
Notes: The primary presentation is eight substantive slides, 3--10. It gives a complete semantic review arc: the original obstruction, bounded negative mechanism screens, operational-information backtracking, revised representation claim, supported physical family, memory/exact-state construction and its remaining gaps. Four further substantive slides supply technical examples for expert conversation without adding slides beyond the requested twelve-page substantive limit.
Sources:
temp_content/feedback/feedback.md

## Slide 3
Which traffic detail matters for control?
A physical traffic effect is only the start of a control-relevant claim.
1. What traffic detail is unresolved, or lost by a declared model?
2. Can that detail change useful common ramp-rate decisions?
3. Can its gradient predict improvement in complete system time?
Keep genuine tasks and strong rivals; add assumptions only with justification.
Separate physical support, state adequacy, control relevance and useful gradients.
Notes: Begin with the question left open last week, not a progress log. Originally we sought traffic detail unresolved after all admitted aggregate mass, flow, supported speed, ramp and control history, which also changed useful common ramp-rate actions under complete all-stream TST. This week checked why that task did not follow from physical merge effects, then explicitly backtracked to model-reduction adequacy. The general research motivation survives, but the original hidden-history claim is not established. Forward fidelity, derivative correctness and useful decisions are separate. A compact sufficient model is an acceptable outcome. Use the source and small analytical certificates before any implementation or experiment.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm9_99_scoped_closure.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r/semantic_position_in_review_tree.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/baseline_review_scope_check.md

## Slide 4
Equal mass can still reveal the lane split
Observed flow can reveal the very lane split that density alone hides.
Same total mass: 10
Lane 1
2
Lane 2
8
Observed total flow: 14
Same total mass: 10
Lane 1
6
Lane 2
4
Observed total flow: 12
Known complete state + exact public dynamics fix the future.
This is a conditional obstruction, not a claim that all freeway detail is observable.
Notes: Recap the last deck's obstruction, then this week's stronger-history audit. The normalized two-lane free-branch example has known coefficients c1=1, c2=1.5. Masses (2,8) and (6,4) both total 10 but yield flows 14 and 12; in that branch total mass and aggregate flow reconstruct the split. These are normalized algebraic units, not calibrated traffic observations. Subsequent RM9 observer-C work uses section/Edie-supported speed accounting rather than inventing a favorable speed channel. If a complete earlier physical state is uniquely known and the dynamics, controls and forcing are exact and public, deterministic evolution fixes the future. Knowing only aggregate initial statistics is different; congested/history domains were not universally ruled out. Neither equal snapshots nor extra lanes alone certify a lawful full-history/action distinction.
Sources:
misc/slides/weekly_freeway_control_review_20261002_notes.md
misc/selective_discreteness_ramp_metering_review/reporting/rm9_99_scoped_closure.md
misc/selective_discreteness_ramp_metering_review/synthesis/rm9/rm9_separate_resource_and_observer_audit.tex

## Slide 5
Physical support did not settle hiddenness
Recovery and finite merge space are real leads; neither proved useful hiddenness.
Recovery: a slow entrant accelerates
Slow effect → recovery along the road
Finite lane: limited space to merge
Spatial macro can retain location
Missing in both: a lawful residual after full history, linked to a useful rate action.
Backtrack at the obstructing contract before adding more traffic mechanisms.
Notes: RM10 reviewed acceleration/recovery: recovery means how a slow entrant accelerates, encounters traffic and ceases to impose an extra restriction, not that the whole freeway is uncongested. Sources support the mechanism. Some mean/speed/hysteresis models are conditionally sufficient; richer families did not bind genuine initialization, equal full history and different useful common rates. RM11 C0 separately reviewed finite longitudinal merging opportunity with genuine sites, including a two-lane antecedent. Public lane geometry and observed position can be retained by spatial macroscopic competitors. Residual gap/position information and its action relevance remained unestablished. Both bounded reviews closed with scoped negative task admission; neither proved the mechanisms false or all aggregate representations sufficient. The diagrams explain physical leads, not reached matched-history cases.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm10/rm10_70_findings_and_conclusion.md
misc/selective_discreteness_ramp_metering_review/reporting/rm11/c0_findings_and_disposition.md

## Slide 6
Backtracking: from unknown to unrepresented
Known traffic can still be poorly represented by a particular model.
First: ground operational knowledge
Detector inputs ≠ all accessible history
Knowledge contract stayed incomplete
Then: test representation adequacy
Retained detail
Compact state
Same physical scenario, rate choices and full objective; each model evolves its own state.
If a compact summary preserves the response, that is a useful scientific result.
Notes: RM12 Stage 1 BP-I audited a documented operational information domain. Point-detector inputs are not automatically a complete cell-wide observer, but used inputs are better documented than all accessible initial/history knowledge. No justified missing-history witness was admitted. BP-R then explicitly changed the claim: what response does an independently evolving model lose when it compresses a shared known scenario? One local ramp, common bounded upstream rate schedules, public forcing and complete all-stream TST remain. The slow group's condition may be known to every model, each initialized by its declared projection. It is then a question of representation, not private controller information. No repeated feed of future reference trajectories is allowed. Spatial/memory/moment models are strong rivals; a sufficient small summary is a positive result. Backtracking preserves the earlier scoped negatives instead of relabeling them as a newly solved original information question.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_i/findings_and_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r/semantic_position_in_review_tree.md

## Slide 7
A slow merge leaves a moving traffic effect
A slow entrant can hold followers back while empty road opens ahead.
Mainline lanes
Dense followers
Gap ahead
Retained location + constrained speed
Upstream rate permission
Finite ramp; travel and queue
Population stays continuous and conserved; a restriction adds no extra vehicle mass.
Basis: Laval–Daganzo flow and moving effects; the joined task uses explicit adaptations.
Notes: BP-R Stage 3 selected the Laval--Daganzo continuum--particle/multilane hybrid family: lane-wise Kinematic Wave (KW) conservation coupled to selected entrants' constrained speed/position trajectories. Hybrid in this source means macroscopic streams plus selected microscopic kinetics, not merely lane resolution or a discretization. Our approved adaptation keeps continuous vehicle-equivalent population and zero-population restriction metadata. Restrictions are effects of traffic already counted in the field. Upstream continuous effective-rate permission acts before finite ramp propagation; permission is not actual merge discharge or a faithfully resolved binary signal. The mandatory merge uses a fixed ramp receiving share with unused capacity available to other eligible traffic. Mainline discretionary transfers remain sampled. This physical family is literature-supported, but the whole adapted module composition and its necessity/benefit are not source theorems.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/findings_and_reference_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/meter_boundary_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/merge_allocation_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/d2_forward/findings_and_field_gate.md
https://escholarship.org/content/qt8w70q261/qt8w70q261.pdf
https://bpb-us-e1.wpmucdn.com/sites.gatech.edu/dist/f/3571/files/2023/03/merges.pdf

## Slide 8
Recovery outlasts the current entry rate
Stopping new merge entries does not instantly erase an old slow entrant.
Actual merge entries
Existing restriction
Entries stop
Recovery continues
Time after actual merging (schematic)
Event counters can remember creation; congestion makes a simple recovery timer unsafe.
Keep distinct position/speed effects first; test safe reduction after the chain is qualified.
Notes: The Stage 3 primary comparator was a mechanism-oriented present-condition mean service law; the companion was a congestion-triggered dynamic capacity drop model. Both are legitimate families, with different source domains. A's local stationary limits pass, but zero present entries is not a complete transient recovery state; B can impose a drop at sampled onset while the chosen reference has not yet created a moving restriction. These are bounded law/activation mismatches, not a proof that every aggregate model fails. T1 strengthens the primary state to distinguish startup, active effects and recovery. Transfer counter remainders supply supported event creation memory. Event times reconstruct motion only in the restricted free-ahead case; congestion changes recovery. Group counts/means lose position-speed association. M1 expands to spatial/kinetic groups; G1 selects exact distinct signatures first, without an engineering cost criterion or a concurrent reduced-model acceptance condition. Reductions are deferred until the exact reference chain is qualified.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/dual_qualification_findings_and_scope_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/event_memory_findings_and_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/grouped_recovery_findings_and_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/exact_information_findings_and_gate.md

## Slide 9
One traffic state must drive every component
Exact effect records cannot act consistently on a field that has erased their gaps.
Completed spatial field
Retained empty gap
Whole-cell averaging
Same total mass; wrong traffic between effects
Sampled births, queue braking and count attachments now have local certificates.
Alignment review: unchanged averages fail; richer fields give partial constructive support.
One shared field must determine motion, lane transfers and the completed next state.
Notes: Exact-first qualification retained all restriction signatures and own history, then bound sampled insertion E1: completed actual transfers create zero-population descriptors at the regular clock, with own updated counts and donor request-phase speed, no retrospective effect. K.A resolves braking when a queue is encountered, integrates actual distance, carries the ending speed and permits positive recovery at the next regular clock. Traffic counts must adjust for accepted transfers and be rebased on actual section crossing. The alignment ladder examined unchanged interfaces, explicit restriction-aware adaptation and a count/wave representation. Uniform whole-cell fields concretely lose retained empty gaps. Step 2 supports exact local two-record evolution; neither it nor step 3 closes all endogenous transfer/motion/birth interactions. Subsequent own-field transfer work qualifies additional bounded coupled examples. This is constructive partial support, not all-mode or indefinite evolution. The diagram is schematic; no new traffic trajectory is simulated.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/sampled_insertion_findings.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/motion_contact_findings_and_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/joined_step_findings_and_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/alignment_ladder_findings.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/fixed_share_completion_findings_and_gate.md

## Slide 10
A candidate chain; the task remains open
Local checks support the chain; useful gradients are not established.
Rate permission
+ finite ramp
Lane-wise field
↔ moving effects
Shared transfers
+ own counts
Sampled births
+ next state
Established: continuous accounting, selected service rules and local coupled certificates.
Static shared-service check: queue growth alone does not earn extra priority.
Open now: the ordinary traffic profile preserved at the next timestep.
Still needed: repeated evolution, clearance and full-system control response.
Then: fair independent reductions, gradient correctness and decision usefulness.
Notes: This final primary page synthesizes the last completed D2 continuation. The whole-forward contract now consolidates upstream continuous admission, finite ramp propagation, lane-wise first-order field, own request/history sampling, T.A amount allowances, P.A held competition weights, N.A fixed ramp priority/unused receiving, D2 physical sender pooling, K.A old-record motion, accepted counts and completed E1 births. These are approved contract choices, with source/static/local support rather than whole-model adoption. The D2 static allocator has a general slack-resource invariance argument plus 5,832 exact cases, 8,292 strict donor/ramp lifts and 3,716 slack receiver lifts, all pass. This is not a traffic simulation or a whole-network existence result. A completed joint one-step field example includes quota exhaustion, wave contacts, a section crossing and two simultaneous births. The current Q.J.F.R field-carryover decision is open: A preserve completed profile (recommended), B qualify a projection. Autonomous repeated evolution, clearance, reached common-rate complete-TST leverage, independent reductions and derivative usefulness remain missing. Stage 3/67 open, Stage 4 unopened; do not infer mesoscopic necessity.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/d2_forward/findings_and_field_gate.md
misc/selective_discreteness_ramp_metering_review/synthesis/rm12/bp_r_stage3/d2_forward/forward_contract_and_qualification.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/fixed_share_completion_findings_and_gate.md

## Slide 11
Technical: effect creation and recovery
A transfer counter creates an effect record; it never creates extra traffic.
Illustrative threshold: 1 equivalent
0.4: no new record
Then 0.6: one record at the next update
Counter progress persists when entries pause; all accepted mass stays accounted for.
Recovery also needs the traffic ahead: identical mean speeds can evolve differently.
Notes: E1 attaches effects after completed actual transfers, not permission, green pulses or equal-size physical packets. An illustrative unit threshold sees 0.4 then 0.6 equivalents: no birth at the first clock, one at the second. The first amount already entered the population; its counter remainder survives pauses. Small terminal remainders still count in population/exits/TST even if no additional descriptor appears. Several simultaneous descriptors at one point get the same own count and distinct motion signatures, no artificial spacing or extra mass. The second example is the bounded moment-update gap: equal-probability speeds (0,20) and (10,10) have equal mean 10. Clipping individual speeds to an ahead limit of 10 gives means 5 and 10. Thus a mean alone cannot determine this recovery update. This is not a reached ramp-control failure or a proof against all richer compact statistics. Exact distinct records are selected before approximation; underlying moving-restriction trajectories and ordinary conserved traffic remain different parts of the state.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/sampled_insertion_findings.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/event_memory_findings_and_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/grouped_recovery_findings_and_gate.md

## Slide 12
Technical: amounts versus rate ceilings
A 25% lane-change request limits mass; it need not limit instantaneous sending.
Extra direction-specific rate cap
Accepted: shared sending
Accepted mass in the final 0.1 s
Through is blocked; the lateral target is free; the amount allowance is not exhausted.
Queue growth changes availability, not the fixed competition weight or allowed mass.
Notes: This page groups three consecutive closed methodological choices: T.A sampled requests are integrated mass allowances; P.A holds their original competition weights during the public step without a queue bonus; D2 shares the physical donor's available sending among active original requests without an additional theta-times-capacity rate ceiling. N.A still fixes the ramp's geometric share and permits unused receiving redistribution. Weights refresh on the next regular request clock; fulfilling an allowance closes that movement with no retry or enlarged amount. The late-arrival diagnostic is a 30m donor, u=30m/s, 1s step, n=.45eq, sampled lateral fraction .25 and Q=9/14eq/s. Traffic in the first 3m reaches the exit at .9s; through receiving is blocked and lateral receiving free. D1's extra .25Q rate ceiling would serve 9/560=.016071eq; approved D2 serves 9/140=.064286eq, both below d=.1125eq. These are distinct timing laws for the same request, not a hidden-state witness. D1 remains conditionally sound if an independently justified persistent direction-specific instantaneous cap exists. Current evidence does not require it. D2's fixed-weight static queue-invariance result is positive only for the finite allocator, not the whole endogenous evolution.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/transfer_feedback_findings_and_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/quota_allocation_findings_and_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/fixed_share_completion_findings_and_gate.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/d2_forward/findings_and_field_gate.md

## Slide 13
Technical: records do not preserve the field
Where the same mass sits determines when it can reach the transfer port.
Same 30 m cell; 0.45 equivalents; same request and boundary counts
Traffic at the exit
Immediate service; 0.1125 equivalents transferred
Traffic at the entrance
Arrival at 0.9 s; 0.0643 equivalents transferred
A spatial macro model can retain this difference; it is not an identity-necessity result.
Open choice: carry the completed profile, or qualify an explicit numerical reconstruction.
Notes: The latest completed D2 pass supplies this ordinary-field diagnostic. Both 30m donors have mass .45eq, the same fixed-end counts and no restriction records. Their common sampled lateral allowance is .1125eq, through receiving is blocked, lateral receiving is free, and Q=9/14eq/s. The early field has jam density .15eq/m on the last 3m [27,30]. Sending starts immediately and the allowance is exhausted after .175s, giving .1125eq. The late field has the same jam block on [0,3]; its front reaches the exit at .9s and serves Q*.1=9/140=.064286eq. These are admissible first-order field/request diagnostics, not two certified reachable equal-history scenarios. A mass-plus-anchor reconstruction maps them to the same field, so conservation and exact retained records do not imply ordinary profile/timing preservation. A sufficiently resolved macroscopic field can distinguish them. No external exit before the end means one-step population-time is the same; no full-TST benefit or metadata necessity follows. Current Q.J.F.R remains open: A retain completed full profile is recommended; B qualify a finite numerical mass-and-anchor reconstruction is legitimate if its error/reference contract is justified. Neither selected by this presentation.
Sources:
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/d2_forward/findings_and_field_gate.md
misc/selective_discreteness_ramp_metering_review/synthesis/rm12/bp_r_stage3/d2_forward/forward_math.tex

## Slide 14
Technical: the useful-gradient evidence chain
A useful direction must improve complete exit timing, including traffic held back.
Waiting outside
On the ramp
On the mainline
Count every not-yet-exited stream (schematic)
N: remaining vehicle-equivalent mass; J: total system time until every stream clears.
Finish the forward chain and fair reductions, then verify derivatives and decision gains.
Notes: Complete all-stream total system time J is the integral until clearance of the whole not-yet-exited population: outside waiting, the finite ramp and every modeled mainline lane. Vehicle-equivalent seconds are the units. Mean time is J divided by the fixed total cohort mass if needed; this slide uses total time. Relocating waiting from mainline to ramp or outside does not improve this objective unless total exit timing changes. The population curves drawn here are conceptual layers, not calculated trajectories. The general sensitivity path is rate permission to actual admission/travel/queue, accepted transfers and moving effects, exits, then complete J. Structural topology, record membership and creation events require a declared derivative/event contract, not an unsupported global smoothness claim. Exact forward qualification, clearance and a reached intervention-sensitive response come before specific gradients. Strong independent spatial/memory/moment rivals and declared initial projections make the representation comparison fair. AD/finite-difference correctness and independent-reference directional usefulness are later distinct evidence products. No optimizer, SUMO, traffic simulation or numerical gradient was performed for this review or presentation. This is the discussion endpoint, not an automatic Stage 4 opening.
Sources:
misc/selective_discreteness_ramp_metering_review/synthesis/rm12/bp_r_stage3/d2_forward/forward_contract_and_qualification.md
misc/selective_discreteness_ramp_metering_review/reporting/rm12/bp_r_stage3/baseline_review_scope_check.md
misc/selective_discreteness_ramp_metering_review/rm12_30_provisional_four_stage_roadmap.md