## Slide 1
Differentiable Minimal Mesoscopic Traffic Simulation
Weekly implementation update
M0 closure · visualizer · M1 · M2 planning | 4 September 2026

## Slide 2
Contents
01
Milestone 0 closure
02
Headless visualizer and two cases
03
Milestone 1 ordered route-mass ledger
04
Milestone 2 interaction-zone planning

## Slide 3
Milestone 0 closed: trusted differentiable macro backbone
Triangular FD + LTM links
Movement maps + node solver
Continuum signal + rollout
Objectives + gradient checks
Component 0.5 completed signal service; Components 0.6–0.7 closed rollout and evidence.
Continuous vehicle-equivalent mass; fixed topology and phase permissions remain structural.
Hand references → conservation/admissibility → reverse/JVP/finite-difference agreement.
Outcome: a reproducible aggregate baseline against which mesoscopic refinements can be isolated.

## Slide 4
M0_a1 visualizer: make dynamics inspectable
Headless Matplotlib renderer over recorded simulator histories—not a second simulator.
Shows topology, occupancy/storage, boundary flow, queues, signal service, and conservation.
Deterministic frames and manifests support review, regression diagnosis, and presentations.
Branch-isolated optional tool: no change to the accepted M0 numerical path.

## Slide 5
Visualizer case 1: two-link spillback chain
Embedded MP4 at ~1 frame/s; click to play in slide-show mode
Downstream storage fills first.
Receiving falls and constrains upstream inflow.
The queue propagates backward without losing mass.
6 intervals; TST = 21 veh-eq·s; residual = 0.

## Slide 6
Spillback case: what the accounting proves
Arrivals enter source accounting
Resident mass links + source queue
Departures enter sink accounting
Every internal boundary uses the same realized mass as upstream outflow and downstream inflow.
Storage limits receiving; rejected inflow remains upstream rather than being clipped.
Cumulative arrivals = resident mass + cumulative exits at every recorded boundary.
The animation connects the causal queue pattern to an exact zero conservation residual.

## Slide 7
Visualizer case 2: full 2×2 network
Embedded MP4 at ~1 frame/s; click to play in slide-show mode
Four intersections share a network-wide flow history.
Selected and background routes compete through common nodes.
Signals regulate movement service and downstream occupancy.
18 intervals; TST = 550.025 veh-eq·s.

## Slide 8
2×2 grid: network-wide traffic accounting
18 directed links are accounted consistently across sources, internal nodes, and sinks.
Each node movement is simultaneously an input-link exit and output-link entry.
Source queues retain demand rejected by entry capacity; sink totals retain completed mass.
Network identity: generated mass = source queues + link occupancy + cumulative sink exits.
Maximum recorded residual: 7.105×10⁻¹⁵ veh-eq (floating-point scale).

## Slide 9
Milestone 1: why retain ordered route mass?
Macro state continuous totals
+ ordered route ledger continuous mass blocks
Future meso behavior route/order-aware service
Question: retain semantic discreteness without integerizing physical vehicle flow.
Routes remain structural table references; each local entry stores route position and divisible mass.
Current movement is projected from route metadata rather than duplicated in persistent state.

## Slide 10
M1 component chain and accepted interfaces
Route table
Ordered ledger
Movement projection
Split / forward / exact merge
Route-aware rollout
Evidence
One exact ordered authority per location; aggregate LTM remains the physical backbone.
Continuous partial transfers split mass and interpolate eligibility time affinely.
Only adjacent entries with identical route state and continuous timing merge losslessly.
Every component closed through implementation, validation, and user checkpoint.

## Slide 11
M1 case: state, notation, and time boundary
Network and routes source 0 → link 0 ↘ link 2 → link 3 (A) / link 4 (B) source 1 → link 1 ↗
Boundary b complete state after interval [b−1,b) Boundary 0 is empty; Δt = 1 s
Where mass can exist S0/S1 = source queues L0…L4 = link ledgers C = completed route mass
One entry: A@p0 : 0.25 [−1.0,−0.5] route A · position 0 · mass 0.25 veh-eq · front/tail eligibility times in seconds Entries inside [ … ] are ordered downstream-first; the order is exact FIFO metadata.
Route table A: L0 → L2 → L3 B: L1 → L2 → L4 p increments after each node crossing
Nodes are transactions, not storage: during an interval they transfer mass; at a boundary every pack is in S, L, or C.
When a pack enters a link, its eligibility profile is shifted by that link's 1 s free-flow delay.

## Slide 12
M1 case: complete quantitative state evolution
INTERVAL [0,1) → B1 Before transfer at sources: S0=[A 0.25(−1,−0.5), A 0.25(−0.5,0)] S1=[B 0.50(−1,0)] Admit all; shift +1 s; exact-merge A B1: L0=[A@p0 0.50(1,2)] L1=[B@p0 0.50(1,2)]
INTERVAL [1,2) → B2 New S0=[A@p0 0.125(0,1)] New S1=[B@p0 0.125(0,1)] Source entry capacity is zero: retain both L0/L1 cross merge node; p0→p1 B2: S0=A0.125; S1=B0.125 L2=[A 0.50(2,3), B 0.50(2,3)]
INTERVALS [2,4) → B3/B4 Queued 0.125 packs enter L0/L1 L2 order [A,B] is preserved; no merge Diverge projects A→L3, B→L4 B3: L0=A0.125(3,4); L1=B0.125(3,4) L3=A0.50(3,3.5); L4=B0.50(3.5,4) B4: C=[0.50,0.50]; L2=[A0.125,B0.125]
INTERVALS [4,6) → B5/B6 Remaining [A0.125,B0.125] diverges B5: L3=A@p2 0.125(5,5.5) L4=B@p2 0.125(5.5,6) B6: all S/L ledgers empty C=[A 0.625, B 0.625] B7: unchanged terminal check
Closure: generated 1.25 = completed A 0.625 + B 0.625; all queues/links empty; residual = 0. L2 keeps [A,B] and route positions: correct divergence, one exact merge, route mismatch safely not merged.

## Slide 13
M1 key choices and engineering difficulty
Selective discreteness IDs/order fixed; mass continuous
Two synchronized views ledger authority; totals derived
Piecewise AD check stable signatures
The hard boundary is semantic: exact lossless merge is allowed; behavioral compression is not.
Immutable tuples and differentiable tensors must preserve graphs through split/forward operations.
A corrective integration pass repaired coupling evidence without weakening scientific criteria.

## Slide 14
Milestone 2: per-lane cumulative-mass interaction zone
Uₐ aggregate upstream LTM
Zₐ per-lane rank grid + ledger
Node neutral M2 service seam
Physical link is partitioned once: upstream propagation plus downstream lane-local refinement.
Equal-width bins index cumulative traffic mass, not physical distance; partial final bins preserve storage.
M2 builds conservative representation/coupling; M3 owns lane allocation and FIFO/blockage behavior.

## Slide 15
M2 planning: 6 global + 19 component questions
GLOBAL BACKBONE — CLOSED
G1 Physical partition + storage/delay G2 U/Z transfer + time indexing G3 Equal-bin tensor/cache contract G4 Neutral node-service boundary G5 Matched equivalence evidence G6 Differentiability + signatures Closed first; these constrain every component-local decision below.
2.1 GEOMETRY / TOPOLOGY
Q1 Record + reconciliation owner Q2 Per-lane physical heterogeneity Q3 Lane order + permission coverage
2.2 ORDERED LANE STATE
Q1 Lane-ledger record boundary Q2 Commitment map + validation Q3 Exact merge + fragmentation
2.3 RANK GRID
Q1 Bin/partial-capacity schema Q2 Edge convention + signature Q3 Cached-grid ownership
2.4 INTERNAL PHYSICS
Q1 Lane capacity + delays Q2 Commitment-feasible receiving Q3 Zone eligibility representation Q4 Storage roundoff/failure policy
2.5 ROLLOUT
Q1 Scenario/state/result histories Q2 Refined/unrefined orchestration Q3 Boundary conservation context
2.6 EVIDENCE
Q1 Independent scalar-oracle floor Q2 FD/tolerance/signature schema Q3 Artifact + provenance contract
Dependency order: 2.1 → 2.2 → 2.3 → 2.4 → 2.5 → 2.6 Phase B is resolving the interfaces before implementation.